## Slide 1
DPTE® solutions
The 11th Vogel Pharmaceutical Engineering International Forum 2019
Getinge Safe Sterile Transfer System
Disposable vs reusable

## Slide 2: GETINGE La Calhène Center of Excellence for isolators and DPTE®
  Vendôme (France, 41)
  8 600 m2 (92,600 sqf)
  More than 220 employees
  Center of Excellence for isolators since 70’s (3200+ isolators designed and manufactured worldwide)
  The DPTE® inventor
  ISO 9001 V2015 &14001 (LRQA) certified

## Slide 3: GETINGE La Calhène Center of Excellence for isolators and DPTE®
Getinge Sweden AB
PO Box 69
Getinge
SE 310 44 Sweden
+46 35 155500
info@getinge.com
Getinge La Calhène
1 rue du Comté de Donegal
Vendôme
FR 41102 France
+33 254 734 747
Getinge Lancer
30 Boulevard de l'Industrie
Tournefeuille
FR 31170 France
+33 561 151 111

## Slide 4: 50 years of innovations, a long journey!
1967
Animals lab. isolators
1972
Isolator for patient care
1972
Isolator for patient care
1974
Aseptic surgical isolator
1975
Protection of RAMSES 2 mummy
1975
Dressing isolator
1978
Isolator for powder filling
1963
DPTE® transfer system
1981
Isolator for sterility testing
1984
Isolator for parenteral nutrition mixing
1986
Isolator for powder transfer
1987
Isolator for liquid filling
1989
Isolator for Large Volume Parenteral
1992
Isolation of a complete line of cytotoxic product
1998
INVANZ : the longest filling line isolator in the world
1999
Isolator for beverage filling line
1993
Isolator for handling of hazardous powder
1993
DPTE-S : total secure transfer system
2005
ISOTEST isolator for sterility test
2008
STERITRACE - HPV sterilizer
2008
FREJA - Isolator for cytotoxic in hospital
2010
ISOTEST - Isolator with integrated Steritrace
2011
ISOFLEX - Flexible wall isolator with Steritrace
DPTE-XS : eXtra Safe
2012
2015
ISOFLEX-R – Modular aseptic isolator

## Slide 5: Biopharma applications

## Slide 6: BIOPHARMA – 75% of Getinge La Calhène production
Aseptic filling

## Slide 7: DPTE®
DPTE® Alpha – History and functionalities

## Slide 8: DPTE® transfer system – History
1963
1st DPTE® Transfer System is developped by La Calhène for transfer of highly toxic nuclear material
1993
2012
DPTE®-XS is developped for an improved degree of safety with its locking system
DPTE®-S: Alpha door cannot open if the Beta component is not correctly connected or positionned.
The devices cannot be separated if the Alpha-Beta door assembly is open

## Slide 9: DPTE® principe https://www.youtube.com/watch?v=gBnQKd_SYRs
Alpha Part
Beta Part
1. Approach
2. Locking
3. Opening
DPTE® consists of 2 assemblies:
  Alpha flange and alpha door: Alpha part
  Container flange and alpha door: Beta part
2 lip seals meeting at a point
In final, 4 elements mutually shielding each other’s faces, locked together by rotation of the Beta part
After container docking onto Alpha flange, a 60° rotation of the container allows during rotation motion:
  Locking of container with Alpha flange
  Locking of container door with Alpha door
  Unlocking of container door from container flange
Alpha ports can be integrated on:
  Isolators / glove boxes
  RABS
  Clean room walls
  LAF / BSC…
  DN105, 190, 270, 350 (460)

## Slide 10: Rotating DPTE® alpha
Rotation of alpha port instead of beta
For large IBC / vessel docking
For docking of beta parts that can not be rotated

## Slide 11: DPTE® Beta
DPTE® Beta - containers

## Slide 12: DPTE® CONTAINERS

## Slide 13: DPTE® CONTAINERS - Miscellaneous
DPTE® Beta – Reusable devices

## Slide 14: DPTE® LIQUID TRANSFER CONTAINERS - Concept
Autoclave sterilization
Filling Isolator
Sterilization step
Production step
Autoclave chamber
Sterilization of tank and DPTE® together in autoclave
Operation
Filling needle and hose can be sterilized inside DPTE® container
Vent filters for autoclaving

## Slide 15: DPTE® LIQUID TRANSFER CONTAINERS - Concept
SIP sterilization
These containers usually in 316L are mainly used with a filling isolator or RABS or clean room.
They are sterilised along with the tank, diaphragm valve open and with a specific cover (resistant to high pressure)
If necessary, product sterilization filter between thank and container (not possible for suspension)
Silicon J3L seals
Filling Isolator
Sterilization step
Production step
Steam
Sterilization of tank and DPTE® together
Operation
Filling needle and hose usually not sterilized inside DPTE® container

## Slide 16: DPTE® LIQUID TRANSFER CONTAINERS - Example
Photos

## Slide 17: DPTE® CONTAINERS - Accessories
DPTE® Beta – baskets, internal arrangement, trolleys…

## Slide 18: DPTE-BetaBag®
Material - applications

## Slide 19: Getinge Vendôme – Sterile packaging
Cleanroom manufacturing
2 Cleanrooms in Vendôme
More than 1000 m² Controlled Atmosphere Areas
Total traceability of products
100% product inspection
Strict gowning regulations
Over 150,000 DPTE-BetaBag® products manufactured in 2018.
The DPTE-BetaBag® is manufactured in highly regulated ultra-clean conditions and contributes to security in biopharma production.

## Slide 20: DPTE-BetaBag® - various material
Name: DPTE-BetaBag® RTU*
DPTE®: Polyethylene
Diam: 105, 190 & 270 mm
Bag: PE & PU
Gamma sterilization
(RTU*)
Name: DPTE-BetaBag® RTS-PC**
DPTE®: PSU or PC
Diam.: 105 & 190 mm
Bag: HDPE - Tyvek®
Autoclave or ETO
(RTS**)

## Slide 21: DPTE-BetaBag®: more than a bag
DPTE® Security and Leaktightness
The validation of our DPTE-BetaBag® complies with international regulations:
Mechanical validation
- validated for up to 5 connexion / disconnexion
- Leak tight testing of DPTE® beta unit
- Leak tight testing of bag welded onto DPTE®
- Seal strength of the bag
Sterility validation (Gamma irradiation cycle between 25 and 50 kGy)
Microbiological validation
- Bioburden
- Endotoxin level
Particulate validation

## Slide 22: DPTE-BetaBag® - Components transfer
Stoppers, caps, pistons, plastic vials…

## Slide 23: DPTE-BetaBag® - Components transfer
In-house « filling station »…

## Slide 24: DPTE-BetaBag® - Waste management
Stoppers, caps, pistons, plastic vials…

## Slide 25: DPTE-BetaBag® - Single Use – Liquid transfer
Partnerships with liquid transfer experts

## Slide 26: DPTE-BetaBag® - media plate
Isobag® from Merck Millipore

## Slide 27: Transfer Leak Tester TLT for DPTE®
Material - applications

## Slide 28: TLT ( TRANSFER LEAK TESTER)
    Market drivers:
    Compliance to the regulatory and inspection organization.
    The TLT system is used to test the DPTE® systems (Alpha and Beta) prior to or after the production cycles.
    Standard features:
    100Vac to 230Vac (CE & UL compliance).
    Compliant to the FDA 21 CFR part 11 and EU annex 11.
    Full traceability recorded on SQL Database.
    Pipeless and wireless.
    Alpha and Beta transfer test (105, 190, 270, 350)
    Multiple tests can be done simultaneous.
    Customer IT connectivity available for user access control (ex Active Directory), for SQL Dabase backup, server printer, pdf file records….
    Stand alone or integrated into the isolator for the Alpha transfer (Control and Traceability included in the isolator HMI)
    50µm hole detection

## Slide 29: TLT ( TRANSFER LEAK TESTER)
Plug with inflatable gasket. Wireless and pipeless.
Battery (10 cycles of capacity)
Trolley connected to electrical power and Ethernet port (available) for storage and batteries power loading
Tablet 11.9 inches for control and traceability.
Windows 10 and SQL server 2016.
Push button for gasket command.
Lighting for information and battery status.
Dedicated support for storage and power loading
Notes: Very similar unit